WALKING BOT
By Lucas
May 2025

---
Development Pipeline
- Create code for device
- Compile (change code into 0s and 1s)
- Upload (put the compiled code onto device)
- Have fun!

---
H-bridge
A h bridge is how a motor works. If S1 and S4 are turned on, then the motor will spin one way. If S2 and S3 are turned on, then the motor will spin the other way.
If S1/S2 or S3/S4 are turned on at the same time then the battery will do at least one of these three things:
- Heat up
- Blow up
- Burn your house down
  This is because that connecting the positive and negative of a battery together causes the electricity to go extremely fast between the terminals. When the electricity goes through the motor, the motor creates resistance for the electricity as the electricity has to make the motor spin before it can go back to the other battery terminal.

---
What is a PWM?
A PWM (Pulse Width Modulation) is something that converts digital (on and off) power to analog (any amount of power). It is in every single type of electronic device that has some kind of processer, as it is used for computing things.
For example, if you wanted to get half the power from a 1(max power) a computer would have to use a PWM so that it could find it out. It would do this by saying that 1 was 100 analog power then it sent analog 50 power. This is what H-briges are used for.

---
Schematic

---
Code
#include <WiFi.h>#include <WebServer.h>#include <ESPmDNS.h>#include <WebSocketsServer.h>
WebServer server(80);WebSocketsServer webSocket = WebSocketsServer(81);
void stopMotors(){  analogWrite(13, 0);  analogWrite(12, 0);  analogWrite(14, 0);  analogWrite(27, 0);}
void moveForward(int fspeed){  analogWrite(13, 0);  analogWrite(12, fspeed * 2);  analogWrite(14, 0);  analogWrite(27, fspeed * 2);  Serial.println("Moving forward with speed: " + String(fspeed));  // Add any additional logic for moving forward}
void moveBackward(int bspeed){  analogWrite(13, bspeed * 2);  analogWrite(12, 0);  analogWrite(14, bspeed * 2);  analogWrite(27, 0);}
void turnLeft(int lspeed){  analogWrite(13, 0);  analogWrite(12, lspeed * 2.5);  analogWrite(14, lspeed * 2.5);  analogWrite(27, 0);}
void turnRight(int rspeed){  analogWrite(13, rspeed * 2.5);  analogWrite(12, 0);  analogWrite(14, 0);  analogWrite(27, rspeed * 2.5);}
void setHue(int hue) {  Serial.print("Set hue to: ");  Serial.println(hue);}
void stopAction() {  stopMotors();}
void moveForwardAction() {  moveForward(255);}
void forwardBackward(int FBValue) {  if(FBValue >= 0)    moveForward(FBValue);  else    moveBackward(-FBValue);}
void leftRightAction(int LRValue) {  if(LRValue >= 0)    turnRight(LRValue);  else    turnLeft(-LRValue);}
void webSocketEvent(uint8_t num, WStype_t type, uint8_t * payload, size_t length) {  if (type == WStype_TEXT) {    String msg = String((char*)payload);    int commaIndex = msg.indexOf(',');    String cmd, valStr;    int value = 0;    bool hasValue = false;    if (commaIndex > 0) {      cmd = msg.substring(0, commaIndex);      valStr = msg.substring(commaIndex + 1);      valStr.trim();      if (valStr.length() > 0) {        value = valStr.toInt();        hasValue = true;      }    } else {      cmd = msg;      cmd.trim();    }
    if (cmd == "hue" && hasValue) {      setHue(value);    } else if (cmd == "fb" && hasValue) {      forwardBackward(value);    } else if (cmd == "lr" && hasValue) {      leftRightAction(value);    } else if (cmd == "stop") {      stopAction();    } else if (cmd == "start") {      moveForwardAction();    } else {      Serial.println("Unknown command received");    }    webSocket.sendTXT(num, "ESP32 got: " + msg);  }}
void handleRoot() {  Serial.println("Request for root path received");  server.send(200, "text/html", R"rawliteral(<!DOCTYPE html><html lang="en">  <head>    <meta charset="UTF-8">    <title>Robium Controller</title>  </head>  <body>    <div class="svg-container">      <svg         width="136.90706mm"         height="82.806686mm"         viewBox="0 0 136.90706 82.806686"         version="1.1"         id="svg1"         inkscape:version="1.4 (86a8ad7, 2024-10-11)"         sodipodi:docname="Joystic.svg"         xmlns:inkscape="http://www.inkscape.org/namespaces/inkscape"         xmlns:sodipodi="http://sodipodi.sourceforge.net/DTD/sodipodi-0.dtd"         xmlns="http://www.w3.org/2000/svg"         xmlns:svg="http://www.w3.org/2000/svg">        <sodipodi:namedview           id="namedview1"           pagecolor="#ffffff"           bordercolor="#000000"           borderopacity="0.25"           inkscape:showpageshadow="2"           inkscape:pageopacity="0.0"           inkscape:pagecheckerboard="0"           inkscape:deskcolor="#d1d1d1"           inkscape:document-units="mm"           inkscape:zoom="1.4378367"           inkscape:cx="387.73527"           inkscape:cy="217.3404"           inkscape:window-width="1920"           inkscape:window-height="1009"           inkscape:window-x="-8"           inkscape:window-y="-8"           inkscape:window-maximized="1"           inkscape:current-layer="layer1"           showguides="true" />        <defs           id="defs1">          <meshgradient             inkscape:collect="always"             id="meshgradient14"             gradientUnits="userSpaceOnUse"             x="26.130112"             y="73.973984">            <meshrow               id="meshrow14">              <meshpatch                 id="meshpatch14">                <stop                   path="c 45.6357,0  91.2714,0  136.907,0"                   style="stop-color:#d7d7d7;stop-opacity:1"                   id="stop15" />                <stop                   path="c 0,27.6022  0,55.2045  0,82.8067"                   style="stop-color:#666666;stop-opacity:1"                   id="stop16" />                <stop                   path="c -45.6357,0  -91.2714,0  -136.907,0"                   style="stop-color:#e7e7e7;stop-opacity:1"                   id="stop17" />                <stop                   path="c 0,-27.6022  0,-55.2045  0,-82.8067"                   style="stop-color:#666666;stop-opacity:1"                   id="stop18" />              </meshpatch>            </meshrow>          </meshgradient>          <linearGradient id="rainbow-gradient" x1="0%" y1="0%" x2="100%" y2="0%">              <stop offset="0%"   stop-color="#FF0000"/>              <stop offset="16%"  stop-color="#FF7F00"/>              <stop offset="33%"  stop-color="#FFFF00"/>              <stop offset="50%"  stop-color="#00FF00"/>              <stop offset="66%"  stop-color="#0000FF"/>              <stop offset="83%"  stop-color="#4B0082"/>              <stop offset="100%" stop-color="#8B00FF"/>          </linearGradient>        </defs>        <g inkscape:label="Layer 1"           inkscape:groupmode="layer"           id="layer1"           transform="translate(-26.130112,-73.973984)">          <rect             style="fill:url(#meshgradient14);fill-opacity:1;stroke-width:0.303295"             id="rect1"             width="136.90706"             height="82.806686"             x="26.130112"             y="73.973984" />          <rect style="fill:url(#rainbow-gradient);fill-opacity:1;stroke-width:0.272325;cursor:pointer;"             id="rect36"             width="125.11385"             height="8.1891403"             x="32.026714"             y="82.04776" />          <g id="g59" style="cursor: pointer;">            <path               style="fill:#e7e7e7;fill-opacity:1;stroke-width:0.3"               d="m 60.38299,124.80323 -14.846639,14.84664 a 21.161711,21.161711 0 0 0 14.826485,6.13658 21.161711,21.161711 0 0 0 14.846122,-6.15725 z"               id="path25" />            <path               style="fill:#e7e7e7;fill-opacity:1;stroke-width:0.3"               d="m 60.362836,103.46294 a 21.161711,21.161711 0 0 0 -14.846639,6.15724 l 14.866793,14.8668 14.883329,-14.88333 a 21.161711,21.161711 0 0 0 -14.903483,-6.14071 z"               id="path18" />            <circle               style="fill:#333333;fill-opacity:1;stroke-width:0.21238"               id="circle18"               cx="60.362579"               cy="124.62481"               r="14.981098" />            <path               id="circle19"               style="fill:#333333;fill-opacity:1;stroke-width:0.295388"               d="m 60.362574,103.78836 a 20.836416,20.836416 0 0 0 -20.83645,20.83645 20.836416,20.836416 0 0 0 20.83645,20.83645 20.836416,20.836416 0 0 0 20.83646,-20.83645 20.836416,20.836416 0 0 0 -20.83646,-20.83645 z m 0,0.22789 a 20.608709,20.608709 0 0 1 20.60908,20.60856 20.608709,20.608709 0 0 1 -20.60908,20.60856 20.608709,20.608709 0 0 1 -20.608557,-20.60856 20.608709,20.608709 0 0 1 20.608557,-20.60856 z" />            <path               id="path20"               style="fill:#333333;fill-opacity:1;stroke-width:0.31691"               d="m 60.362573,102.27024 a 22.354536,22.354536 0 0 0 -22.354572,22.35457 22.354536,22.354536 0 0 0 22.354572,22.35457 22.354536,22.354536 0 0 0 22.354583,-22.35457 22.354536,22.354536 0 0 0 -22.354583,-22.35457 z m 0,0.24449 A 22.110238,22.110238 0 0 1 82.47321,124.62481 22.110238,22.110238 0 0 1 60.362573,146.73489 22.110238,22.110238 0 0 1 38.252498,124.62481 22.110238,22.110238 0 0 1 60.362573,102.51473 Z" />            <rect               style="fill:#ffffff;fill-opacity:1;stroke-width:0.171085"               id="rect20"               width="0.15741065"               height="29.960497"               x="130.21555"               y="31.906748"               transform="rotate(44.365062)" />            <rect               style="fill:#ffffff;fill-opacity:1;stroke-width:0.171085"               id="rect21"               width="0.15741065"               height="29.960497"               x="43.704025"               y="-146.35017"               transform="rotate(135.72446)" />            <circle               style="fill:#ffffff;fill-opacity:1;stroke-width:0.3"               id="path26"               cx="60.362579"               cy="124.62481"               r="4.5083642" />            <path               id="path27"               style="fill:#ffffff;fill-opacity:1;stroke-width:0.0739703"               d="m 60.362577,119.40698 a 5.2178191,5.2178191 0 0 0 -5.217827,5.21783 5.2178191,5.2178191 0 0 0 5.217827,5.21782 5.2178191,5.2178191 0 0 0 5.21783,-5.21782 5.2178191,5.2178191 0 0 0 -5.21783,-5.21783 z m 0,0.057 a 5.160797,5.160797 0 0 1 5.16089,5.16077 5.160797,5.160797 0 0 1 -5.16089,5.16076 5.160797,5.160797 0 0 1 -5.160758,-5.16076 5.160797,5.160797 0 0 1 5.160758,-5.16077 z" />          </g>          <g id="g37"             transform="translate(2.886857,3.5430299)">            <text               xml:space="preserve"               style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#f9f9f9;fill-opacity:1;stroke-width:0.3"               x="48.027882"               y="96.42379"               id="text36">              <tspan sodipodi:role="line" id="tspan36" style="font-size:3.52778px;stroke-width:0.3" x="48.027882" y="96.42379">Value:</tspan>            </text>            <text               xml:space="preserve"               style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#000000;fill-opacity:1;stroke-width:0.3"               x="59.669559"               y="96.42379"               id="text37">              <tspan sodipodi:role="line" id="tspan37" style="font-size:3.52778px;fill:#000000;stroke-width:0.3" x="59.669559" y="96.42379">100</tspan>            </text>          </g>          <g id="g60" style="cursor: pointer;">            <path               style="fill:#e7e7e7;fill-opacity:1;stroke-width:0.3"               d="m 128.62629,124.6452 -14.84664,-14.84664 a 21.161711,21.161711 0 0 0 -6.13658,14.82648 21.161711,21.161711 0 0 0 6.15725,14.84612 z"               id="path28" />            <path               style="fill:#e7e7e7;fill-opacity:1;stroke-width:0.3"               d="m 149.96658,124.62504 a 21.161711,21.161711 0 0 0 -6.15724,-14.84664 l -14.8668,14.8668 14.88333,14.88332 a 21.161711,21.161711 0 0 0 6.14071,-14.90348 z"               id="path29" />            <circle               style="fill:#333333;fill-opacity:1;stroke-width:0.21238"               id="circle29"               cx="124.62479"               cy="-128.80472"               r="14.981098"               transform="rotate(90)" />            <path               id="path30"               style="fill:#333333;fill-opacity:1;stroke-width:0.295388"               d="m 149.64116,124.62478 a 20.836416,20.836416 0 0 0 -20.83645,-20.83645 20.836416,20.836416 0 0 0 -20.83645,20.83645 20.836416,20.836416 0 0 0 20.83645,20.83646 20.836416,20.836416 0 0 0 20.83645,-20.83646 z m -0.22789,0 a 20.608709,20.608709 0 0 1 -20.60856,20.60908 20.608709,20.608709 0 0 1 -20.60856,-20.60908 20.608709,20.608709 0 0 1 20.60856,-20.60856 20.608709,20.608709 0 0 1 20.60856,20.60856 z"               />            <path               id="path31"               style="fill:#333333;fill-opacity:1;stroke-width:0.31691"               d="m 151.15928,124.62478 a 22.354536,22.354536 0 0 0 -22.35457,-22.35457 22.354536,22.354536 0 0 0 -22.35457,22.35457 22.354536,22.354536 0 0 0 22.35457,22.35458 22.354536,22.354536 0 0 0 22.35457,-22.35458 z m -0.24448,0 a 22.110238,22.110238 0 0 1 -22.11009,22.11064 22.110238,22.110238 0 0 1 -22.11008,-22.11064 22.110238,22.110238 0 0 1 22.11008,-22.11008 22.110238,22.110238 0 0 1 22.11009,22.11008 z"               />            <rect               style="fill:#ffffff;fill-opacity:1;stroke-width:0.171085"               id="rect31"               width="0.15741065"               height="29.960497"               x="-1.0483481"               y="-194.20372"               transform="rotate(134.36506)" />            <rect               style="fill:#ffffff;fill-opacity:1;stroke-width:0.171085"               id="rect32"               width="0.15741065"               height="29.960497"               x="-179.22873"               y="-9.7590256"               transform="rotate(-134.27554)" />            <circle               style="fill:#ffffff;fill-opacity:1;stroke-width:0.3"               id="circle32"               cx="124.62479"               cy="-128.80472"               r="4.5083642"               transform="rotate(90)" />            <path               id="path32"               style="fill:#ffffff;fill-opacity:1;stroke-width:0.0739703"               d="m 134.02254,124.62478 a 5.2178191,5.2178191 0 0 0 -5.21783,-5.21782 5.2178191,5.2178191 0 0 0 -5.21782,5.21782 5.2178191,5.2178191 0 0 0 5.21782,5.21783 5.2178191,5.2178191 0 0 0 5.21783,-5.21783 z m -0.057,0 a 5.160797,5.160797 0 0 1 -5.16077,5.16089 5.160797,5.160797 0 0 1 -5.16076,-5.16089 5.160797,5.160797 0 0 1 5.16076,-5.16076 5.160797,5.160797 0 0 1 5.16077,5.16076 z"               />          </g>          <g id="g39"             transform="translate(71.141387,3.5430299)">            <text               xml:space="preserve"               style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#f9f9f9;fill-opacity:1;stroke-width:0.3"               x="48.027882"               y="96.42379"               id="text38">              <tspan sodipodi:role="line" id="tspan38" style="font-size:3.52778px;stroke-width:0.3" x="48.027882" y="96.42379">Value:</tspan>            </text>            <text               xml:space="preserve"               style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#000000;fill-opacity:1;stroke-width:0.3"               x="59.669559"               y="96.42379"               id="text39">              <tspan sodipodi:role="line" id="tspan39" style="font-size:3.52778px;fill:#000000;stroke-width:0.3" x="59.669559" y="96.42379">100</tspan>            </text>          </g>          <g id="g41"             transform="translate(40.323936,-17.02088)">            <g id="g53">              <text                 xml:space="preserve"                 style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#f9f9f9;fill-opacity:1;stroke-width:0.3"                 x="42.207043"                 y="96.42379"                 id="text40">                <tspan sodipodi:role="line" id="tspan40" style="font-size:3.52778px;stroke-width:0.3" x="42.207043" y="96.42379">Value Hue:</tspan>              </text>              <text                 xml:space="preserve"                 style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#000000;fill-opacity:1;stroke-width:0.3"                 x="59.669559"                 y="96.42379"                 id="text41">                <tspan sodipodi:role="line" id="tspan41" style="font-size:3.52778px;fill:#000000;stroke-width:0.3" x="59.669559" y="96.42379"> 100</tspan>              </text>            </g>          </g>          <path             id="rect41"             style="fill:#333333;fill-opacity:1;stroke-width:0.283737"             d="M 36.894906,82.047615 V 90.9528 h -0.134359 v 1.989331 h 0.544669 V 90.9528 h -0.134358 v -8.905185 z" />          <g id="g57"  style="cursor:pointer;">            <circle               style="fill:#333333;fill-opacity:1;stroke-width:0.21"               id="path42"               cx="86.958687"               cy="146.61284"               r="5.9203753" />            <path               id="path47"               style="fill:#ffffff;fill-opacity:1;stroke-width:0.0739703"               d="m 86.95869,141.39506 a 5.2178191,5.2178191 0 0 0 -5.217827,5.21783 5.2178191,5.2178191 0 0 0 5.217827,5.21782 5.2178191,5.2178191 0 0 0 5.21783,-5.21782 5.2178191,5.2178191 0 0 0 -5.21783,-5.21783 z m 0,0.057 a 5.160797,5.160797 0 0 1 5.16089,5.16077 5.160797,5.160797 0 0 1 -5.16089,5.16076 5.160797,5.160797 0 0 1 -5.160758,-5.16076 5.160797,5.160797 0 0 1 5.160758,-5.16077 z" />            <g id="g48"               transform="translate(29.785713,56.955833)">              <text                 xml:space="preserve"                 style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#f9f9f9;fill-opacity:1;stroke-width:0.3"                 x="53.502323"                 y="90.581314"                 id="text47">                <tspan sodipodi:role="line" id="tspan47" style="font-size:3.52778px;stroke-width:0.3" x="53.502323" y="90.581314">Stop</tspan>              </text>            </g>          </g>          <g id="g58" style="cursor:pointer;">            <circle               style="fill:#333333;fill-opacity:1;stroke-width:0.21"               id="circle48"               cx="102.2086"               cy="146.61284"               r="5.9203753" />            <path               id="path48"               style="fill:#ffffff;fill-opacity:1;stroke-width:0.0739703"               d="m 102.20859,141.39506 a 5.2178191,5.2178191 0 0 0 -5.217819,5.21783 5.2178191,5.2178191 0 0 0 5.217819,5.21782 5.2178191,5.2178191 0 0 0 5.21783,-5.21782 5.2178191,5.2178191 0 0 0 -5.21783,-5.21783 z m 0,0.057 a 5.160797,5.160797 0 0 1 5.16089,5.16077 5.160797,5.160797 0 0 1 -5.16089,5.16076 5.160797,5.160797 0 0 1 -5.16075,-5.16076 5.160797,5.160797 0 0 1 5.16075,-5.16077 z" />            <g id="g49"               transform="translate(44.72165,56.955833)">              <text                 xml:space="preserve"                 style="font-size:3.52778px;line-height:1.3;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;text-align:start;
writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#f9f9f9;fill-opacity:1;stroke-width:0.3"                 x="53.502323"                 y="90.581314"                 id="text48">                <tspan sodipodi:role="line" id="tspan48" style="font-size:3.52778px;stroke-width:0.3" x="53.502323" y="90.581314">Start</tspan>              </text>            </g>          </g>          <path             id="rect52"             style="fill:#333333;fill-opacity:1;stroke-width:0.289062"             d="m 31.53555,81.565092 v 9.15448 h 126.09618 v -9.15448 z m 0.275953,0.29869 H 157.35577 v 8.5571 H 31.811503 Z" />          <path             id="path56"             style="fill:#333333;fill-opacity:1;stroke-width:0.289062"             d="M 26.553015,74.598907 V 156.15575 H 162.61427 V 74.598907 Z m 0.275953,0.29869 H 162.33831 V 155.85706 H 26.828968 Z"             sodipodi:nodetypes="cccccccccc" />          <text             xml:space="preserve"             style="font-style:italic;font-size:2.11667px;line-height:0.6;font-family:Ubuntu;-inkscape-font-specification:'Ubuntu Italic';text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#000000;fill-opacity:1;stroke-width:0.3"             x="134.54373"             y="79.408203"             id="text1">            <tspan sodipodi:role="line" id="tspan1" style="font-style:normal;font-variant:normal;font-weight:normal;font-stretch:normal;font-size:2.11667px;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;fill:#000000;fill-opacity:1;stroke-width:0.3" x="134.54373" y="79.408203">Status: </tspan>          </text>          <text             xml:space="preserve"             style="font-style:italic;font-size:2.11667px;line-height:0.6;font-family:Ubuntu;-inkscape-font-specification:'Ubuntu Italic';text-align:start;writing-mode:lr-tb;direction:ltr;text-anchor:start;fill:#000000;fill-opacity:1;stroke-width:0.3"             x="141.95197"             y="79.408203"             id="text2">            <tspan sodipodi:role="line" id="tspan2" style="font-style:normal;font-variant:normal;font-weight:normal;font-stretch:normal;font-size:2.11667px;font-family:Ubuntu;-inkscape-font-specification:Ubuntu;fill:#000000;fill-opacity:1;stroke-width:0.3" x="141.95197" y="79.408203">Connecting... </tspan>          </text>        </g>        <script           id="mesh_polyfill"           type="text/javascript">          /* [The complete mesh polyfill JS code as in your file] */          !function(){const t="http://www.w3.org/2000/svg",e="http://www.w3.org/1999/xlink",s="http://www.w3.org/1999/xhtml",r=2;if(document.createElementNS(t,"meshgradient").x)return;const n=(t,e,s,r)=>{let n=new x(.5*(e.x+s.x),.5*(e.y+s.y)),o=new x(.5*(t.x+e.x),.5*(t.y+e.y)),i=new x(.5*(s.x+r.x),.5*(s.y+r.y)),a=new x(.5*(n.x+o.x),.5*(n.y+o.y)),h=new x(.5*(n.x+i.x),.5*(n.y+i.y)),l=new x(.5*(a.x+h.x),.5*(a.y+h.y));return[[t,o,a,l],[l,h,i,r]]},o=t=>{let e=t[0].distSquared(t[1]),s=t[2].distSquared(t[3]),r=.25*t[0].distSquared(t[2]),n=.25*t[1].distSquared(t[3]),o=e>s?e:s,i=r>n?r:n;return 18*(o>i?o:i)},i=(t,e)=>Math.sqrt(t.distSquared(e)),a=(t,e)=>t.scale(2/3).add(e.scale(1/3)),h=t=>{let e,s,r,n,o,i,a,h=new g;return t.match(/(w+(s*[^)]+))+/g).forEach(t=>{let l=t.match(/[w.-]+/g),d=l.shift();switch(d){case"translate":2===l.length?e=new g(1,0,0,1,l[0],l[1]):(console.error("mesh.js: translate does not have 2 arguments!"),e=new g(1,0,0,1,0,0)),h=h.append(e);break;case"scale":1===l.length?s=new g(l[0],0,0,l[0],0,0):2===l.length?s=new g(l[0],0,0,l[1],0,0):(console.error("mesh.js: scale does not have 1 or 2 arguments!"),s=new g(1,0,0,1,0,0)),h=h.append(s);break;case"rotate":if(3===l.length&&(e=new g(1,0,0,1,l[1],l[2]),h=h.append(e)),l[0]){r=l[0]*Math.PI/180;let t=Math.cos(r),e=Math.sin(r);Math.abs(t)<1e-16&&(t=0),Math.abs(e)<1e-16&&(e=0),a=new g(t,e,-e,t,0,0),h=h.append(a)}else console.error("math.js: No argument to rotate transform!");3===l.length&&(e=new g(1,0,0,1,-l[1],-l[2]),h=h.append(e));break;case"skewX":l[0]?(r=l[0]*Math.PI/180,n=Math.tan(r),o=new g(1,0,n,1,0,0),h=h.append(o)):console.error("math.js: No argument to skewX transform!");break;case"skewY":l[0]?(r=l[0]*Math.PI/180,n=Math.tan(r),i=new g(1,n,0,1,0,0),h=h.append(i)):console.error("math.js: No argument to skewY transform!");break;case"matrix":6===l.length?h=h.append(new g(...l)):console.error("math.js: Incorrect number of arguments for matrix!");break;default:console.error("mesh.js: Unhandled transform type: "+d)}}),h},l=t=>{let e=[],s=t.split(/[ ,]+/);for(let t=0,r=s.length-1;t<r;t+=2)e.push(new x(parseFloat(s[t]),parseFloat(s[t+1])));return e},d=(t,e)=>{for(let s in e)t.setAttribute(s,e[s])},c=(t,e,s,r,n)=>{let o,i,a=[0,0,0,0];for(let h=0;h<3;++h)e[h]<t[h]&&e[h]<s[h]||t[h]<e[h]&&s[h]<e[h]?a[h]=0:(a[h]=.5*((e[h]-t[h])/r+(s[h]-e[h])/n),o=Math.abs(3*(e[h]-t[h])/r),i=Math.abs(3*(s[h]-e[h])/n),a[h]>o?a[h]=o:a[h]>i&&(a[h]=i));return a},u=[[1,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0],[0,0,0,0,1,0,0,0,0,0,0,0,0,0,0,0],[-3,3,0,0,-2,-1,0,0,0,0,0,0,0,0,0,0],[2,-2,0,0,1,1,0,0,0,0,0,0,0,0,0,0],[0,0,0,0,0,0,0,0,1,0,0,0,0,0,0,0],[0,0,0,0,0,0,0,0,0,0,0,0,1,0,0,0],[0,0,0,0,0,0,0,0,-3,3,0,0,-2,-1,0,0],[0,0,0,0,0,0,0,0,2,-2,0,0,1,1,0,0],[-3,0,3,0,0,0,0,0,-2,0,-1,0,0,0,0,0],[0,0,0,0,-3,0,3,0,0,0,0,0,-2,0,-1,0],[9,-9,-9,9,6,3,-6,-3,6,-6,3,-3,4,2,2,1],[-6,6,6,-6,-3,-3,3,3,-4,4,-2,2,-2,-2,-1,-1],[2,0,-2,0,0,0,0,0,1,0,1,0,0,0,0,0],[0,0,0,0,2,0,-2,0,0,0,0,0,1,0,1,0],[-6,6,6,-6,-4,-2,4,2,-3,3,-3,3,-2,-1,-2,-1],[4,-4,-4,4,2,2,-2,-2,2,-2,2,-2,1,1,1,1]],f=t=>{let e=[];for(let s=0;s<16;++s){e[s]=0;for(let r=0;r<16;++r)e[s]+=u[s][r]*t[r]}return e},p=(t,e,s)=>{const r=e*e,n=s*s,o=e*e*e,i=s*s*s;return t[0]+t[1]*e+t[2]*r+t[3]*o+t[4]*s+t[5]*s*e+t[6]*s*r+t[7]*s*o+t[8]*n+t[9]*n*e+t[10]*n*r+t[11]*n*o+t[12]*i+t[13]*i*e+t[14]*i*r+t[15]*i*o},y=t=>{let e=[],s=[],r=[];for(let s=0;s<4;++s)e[s]=[],e[s][0]=n(t[0][s],t[1][s],t[2][s],t[3][s]),e[s][1]=[],e[s][1].push(...n(...e[s][0][0])),e[s][1].push(...n(...e[s][0][1])),e[s][2]=[],e[s][2].push(...n(...e[s][1][0])),e[s][2].push(...n(...e[s][1][1])),e[s][2].push(...n(...e[s][1][2])),e[s][2].push(...n(...e[s][1][3]));for(let t=0;t<8;++t){s[t]=[];for(let r=0;r<4;++r)s[t][r]=[],s[t][r][0]=n(e[0][2][t][r],e[1][2][t][r],e[2][2][t][r],e[3][2][t][r]),s[t][r][1]=[],s[t][r][1].push(...n(...s[t][r][0][0])),s[t][r][1].push(...n(...s[t][r][0][1])),s[t][r][2]=[],s[t][r][2].push(...n(...s[t][r][1][0])),s[t][r][2].push(...n(...s[t][r][1][1])),s[t][r][2].push(...n(...s[t][r][1][2])),s[t][r][2].push(...n(...s[t][r][1][3]))}for(let t=0;t<8;++t){r[t]=[];for(let e=0;e<8;++e)r[t][e]=[],r[t][e][0]=s[t][0][2][e],r[t][e][1]=s[t][1][2][e],r[t][e][2]=s[t][2][2][e],r[t][e][3]=s[t][3][2][e]}return r};class x{constructor(t,e){this.x=t||0,this.y=e||0}toString(){return`(x=undefined, y=undefined)`}clone(){return new x(this.x,this.y)}add(t){return new x(this.x+t.x,this.y+t.y)}scale(t){return void 0===t.x?new x(this.x*t,this.y*t):new x(this.x*t.x,this.y*t.y)}distSquared(t){let e=this.x-t.x,s=this.y-t.y;return e*e+s*s}transform(t){let e=this.x*t.a+this.y*t.c+t.e,s=this.x*t.b+this.y*t.d+t.f;return new x(e,s)}}class g{constructor(t,e,s,r,n,o){void 0===t?(this.a=1,this.b=0,this.c=0,this.d=1,this.e=0,this.f=0):(this.a=t,this.b=e,this.c=s,this.d=r,this.e=n,this.f=o)}toString(){return`affine: undefined undefined undefined       undefined undefined undefined`}append(t){t instanceof g||console.error("mesh.js: argument to Affine.append is not affine!");let e=this.a*t.a+this.c*t.b,s=this.b*t.a+this.d*t.b,r=this.a*t.c+this.c*t.d,n=this.b*t.c+this.d*t.d,o=this.a*t.e+this.c*t.f+this.e,i=this.b*t.e+this.d*t.f+this.f;return new g(e,s,r,n,o,i)}}class w{constructor(t,e){this.nodes=t,this.colors=e}paintCurve(t,e){if(o(this.nodes)>r){const s=n(...this.nodes);let r=[[],[]],o=[[],[]];for(let t=0;t<4;++t)r[0][t]=this.colors[0][t],r[1][t]=(this.colors[0][t]+this.colors[1][t])/2,o[0][t]=r[1][t],o[1][t]=this.colors[1][t];let i=new w(s[0],r),a=new w(s[1],o);i.paintCurve(t,e),a.paintCurve(t,e)}else{let s=Math.round(this.nodes[0].x);if(s>=0&&s<e){let r=4*(~~this.nodes[0].y*e+s);t[r]=Math.round(this.colors[0][0]),t[r+1]=Math.round(this.colors[0][1]),t[r+2]=Math.round(this.colors[0][2]),t[r+3]=Math.round(this.colors[0][3])}}}}class m{constructor(t,e){this.nodes=t,this.colors=e}split(){let t=[[],[],[],[]],e=[[],[],[],[]],s=[[[],[]],[[],[]]],r=[[[],[]],[[],[]]];for(let s=0;s<4;++s){const r=n(this.nodes[0][s],this.nodes[1][s],this.nodes[2][s],this.nodes[3][s]);t[0][s]=r[0][0],t[1][s]=r[0][1],t[2][s]=r[0][2],t[3][s]=r[0][3],e[0][s]=r[1][0],e[1][s]=r[1][1],e[2][s]=r[1][2],e[3][s]=r[1][3]}for(let t=0;t<4;++t)s[0][0][t]=this.colors[0][0][t],s[0][1][t]=this.colors[0][1][t],s[1][0][t]=(this.colors[0][0][t]+this.colors[1][0][t])/2,s[1][1][t]=(this.colors[0][1][t]+this.colors[1][1][t])/2,r[0][0][t]=s[1][0][t],r[0][1][t]=s[1][1][t],r[1][0][t]=this.colors[1][0][t],r[1][1][t]=this.colors[1][1][t];return[new m(t,s),new m(e,r)]}paint(t,e){let s,n=!1;for(let t=0;t<4;++t)if((s=o([this.nodes[0][t],this.nodes[1][t],this.nodes[2][t],this.nodes[3][t]]))>r){n=!0;break}if(n){let s=this.split();s[0].paint(t,e),s[1].paint(t,e)}else{new w([...this.nodes[0]],[...this.colors[0]]).paintCurve(t,e)}}}class b{constructor(t){this.readMesh(t),this.type=t.getAttribute("type")||"bilinear"}readMesh(t){let e=[[]],s=[[]],r=Number(t.getAttribute("x")),n=Number(t.getAttribute("y"));e[0][0]=new x(r,n);let o=t.children;for(let t=0,r=o.length;t<r;++t){e[3*t+1]=[],e[3*t+2]=[],e[3*t+3]=[],s[t+1]=[];let r=o[t].children;for(let n=0,o=r.length;n<o;++n){let o=r[n].children;for(let r=0,i=o.length;r<i;++r){let i=r;0!==t&&++i;let h,d=o[r].getAttribute("path"),c="l";null!=d&&(c=(h=d.match(/s*([lLcC])s*(.*)/))[1]);let u=l(h[2]);switch(c){case"l":0===i?(e[3*t][3*n+3]=u[0].add(e[3*t][3*n]),e[3*t][3*n+1]=a(e[3*t][3*n],e[3*t][3*n+3]),e[3*t][3*n+2]=a(e[3*t][3*n+3],e[3*t][3*n])):1===i?(e[3*t+3][3*n+3]=u[0].add(e[3*t][3*n+3]),e[3*t+1][3*n+3]=a(e[3*t][3*n+3],e[3*t+3][3*n+3]),e[3*t+2][3*n+3]=a(e[3*t+3][3*n+3],e[3*t][3*n+3])):2===i?(0===n&&(e[3*t+3][3*n+0]=u[0].add(e[3*t+3][3*n+3])),e[3*t+3][3*n+1]=a(e[3*t+3][3*n],e[3*t+3][3*n+3]),e[3*t+3][3*n+2]=a(e[3*t+3][3*n+3],e[3*t+3][3*n])):(e[3*t+1][3*n]=a(e[3*t][3*n],e[3*t+3][3*n]),e[3*t+2][3*n]=a(e[3*t+3][3*n],e[3*t][3*n]));break;case"L":0===i?(e[3*t][3*n+3]=u[0],e[3*t][3*n+1]=a(e[3*t][3*n],e[3*t][3*n+3]),e[3*t][3*n+2]=a(e[3*t][3*n+3],e[3*t][3*n])):1===i?(e[3*t+3][3*n+3]=u[0],e[3*t+1][3*n+3]=a(e[3*t][3*n+3],e[3*t+3][3*n+3]),e[3*t+2][3*n+3]=a(e[3*t+3][3*n+3],e[3*t][3*n+3])):2===i?(0===n&&(e[3*t+3][3*n+0]=u[0]),e[3*t+3][3*n+1]=a(e[3*t+3][3*n],e[3*t+3][3*n+3]),e[3*t+3][3*n+2]=a(e[3*t+3][3*n+3],e[3*t+3][3*n])):(e[3*t+1][3*n]=a(e[3*t][3*n],e[3*t+3][3*n]),e[3*t+2][3*n]=a(e[3*t+3][3*n],e[3*t][3*n]));break;case"c":0===i?(e[3*t][3*n+1]=u[0].add(e[3*t][3*n]),e[3*t][3*n+2]=u[1].add(e[3*t][3*n]),e[3*t][3*n+3]=u[2].add(e[3*t][3*n])):1===i?(e[3*t+1][3*n+3]=u[0].add(e[3*t][3*n+3]),e[3*t+2][3*n+3]=u[1].add(e[3*t][3*n+3]),e[3*t+3][3*n+3]=u[2].add(e[3*t][3*n+3])):2===i?(e[3*t+3][3*n+2]=u[0].add(e[3*t+3][3*n+3]),e[3*t+3][3*n+1]=u[1].add(e[3*t+3][3*n+3]),0===n&&(e[3*t+3][3*n+0]=u[2].add(e[3*t+3][3*n+3]))):(e[3*t+2][3*n]=u[0].add(e[3*t+3][3*n]),e[3*t+1][3*n]=u[1].add(e[3*t+3][3*n]));break;case"C":0===i?(e[3*t][3*n+1]=u[0],e[3*t][3*n+2]=u[1],e[3*t][3*n+3]=u[2]):1===i?(e[3*t+1][3*n+3]=u[0],e[3*t+2][3*n+3]=u[1],e[3*t+3][3*n+3]=u[2]):2===i?(e[3*t+3][3*n+2]=u[0],e[3*t+3][3*n+1]=u[1],0===n&&(e[3*t+3][3*n+0]=u[2])):(e[3*t+2][3*n]=u[0],e[3*t+1][3*n]=u[1]);break;default:console.error("mesh.js: "+c+" invalid path type.");}if(0===t&&0===n||r>0){let e=window.getComputedStyle(o[r]).stopColor.match(/^rgbs*(s*(d+)s*,s*(d+)s*,s*(d+)s*)$/i),a=window.getComputedStyle(o[r]).stopOpacity,h=255;a&&(h=Math.floor(255*a)),e&&(0===i?(s[t][n]=[],s[t][n][0]=Math.floor(e[1]),s[t][n][1]=Math.floor(e[2]),s[t][n][2]=Math.floor(e[3]),s[t][n][3]=h):1===i?(s[t][n+1]=[],s[t][n+1][0]=Math.floor(e[1]),s[t][n+1][1]=Math.floor(e[2]),s[t][n+1][2]=Math.floor(e[3]),s[t][n+1][3]=h):2===i?(s[t+1][n+1]=[],s[t+1][n+1][0]=Math.floor(e[1]),s[t+1][n+1][1]=Math.floor(e[2]),s[t+1][n+1][2]=Math.floor(e[3]),s[t+1][n+1][3]=h):3===i&&(s[t+1][n]=[],s[t+1][n][0]=Math.floor(e[1]),s[t+1][n][1]=Math.floor(e[2]),s[t+1][n][2]=Math.floor(e[3]),s[t+1][n][3]=h))}}e[3*t+1][3*n+1]=new x,e[3*t+1][3*n+2]=new x,e[3*t+2][3*n+1]=new x,e[3*t+2][3*n+2]=new x,e[3*t+1][3*n+1].x=(-4*e[3*t][3*n].x+6*(e[3*t][3*n+1].x+e[3*t+1][3*n].x)+-2*(e[3*t][3*n+3].x+e[3*t+3][3*n].x)+3*(e[3*t+3][3*n+1].x+e[3*t+1][3*n+3].x)+-1*e[3*t+3][3*n+3].x)/9,e[3*t+1][3*n+2].x=(-4*e[3*t][3*n+3].x+6*(e[3*t][3*n+2].x+e[3*t+1][3*n+3].x)+-2*(e[3*t][3*n].x+e[3*t+3][3*n+3].x)+3*(e[3*t+3][3*n+2].x+e[3*t+1][3*n].x)+-1*e[3*t+3][3*n].x)/9,e[3*t+2][3*n+1].x=(-4*e[3*t+3][3*n].x+6*(e[3*t+3][3*n+1].x+e[3*t+2][3*n].x)+-2*(e[3*t+3][3*n+3].x+e[3*t][3*n].x)+3*(e[3*t][3*n+1].x+e[3*t+2][3*n+3].x)+-1*e[3*t][3*n+3].x)/9,e[3*t+2][3*n+2].x=(-4*e[3*t+3][3*n+3].x+6*(e[3*t+3][3*n+2].x+e[3*t+2][3*n+3].x)+-2*(e[3*t+3][3*n].x+e[3*t][3*n+3].x)+3*(e[3*t][3*n+2].x+e[3*t+2][3*n].x)+-1*e[3*t][3*n].x)/9,e[3*t+1][3*n+1].y=(-4*e[3*t][3*n].y+6*(e[3*t][3*n+1].y+e[3*t+1][3*n].y)+-2*(e[3*t][3*n+3].y+e[3*t+3][3*n].y)+3*(e[3*t+3][3*n+1].y+e[3*t+1][3*n+3].y)+-1*e[3*t+3][3*n+3].y)/9,e[3*t+1][3*n+2].y=(-4*e[3*t][3*n+3].y+6*(e[3*t][3*n+2].y+e[3*t+1][3*n+3].y)+-2*(e[3*t][3*n].y+e[3*t+3][3*n+3].y)+3*(e[3*t+3][3*n+2].y+e[3*t+1][3*n].y)+-1*e[3*t+3][3*n].y)/9,e[3*t+2][3*n+1].y=(-4*e[3*t+3][3*n].y+6*(e[3*t+3][3*n+1].y+e[3*t+2][3*n].y)+-2*(e[3*t+3][3*n+3].y+e[3*t][3*n].y)+3*(e[3*t][3*n+1].y+e[3*t+2][3*n+3].y)+-1*e[3*t][3*n+3].y)/9,e[3*t+2][3*n+2].y=(-4*e[3*t+3][3*n+3].y+6*(e[3*t+3][3*n+2].y+e[3*t+2][3*n+3].y)+-2*(e[3*t+3][3*n].y+e[3*t][3*n+3].y)+3*(e[3*t][3*n+2].y+e[3*t+2][3*n].y)+-1*e[3*t][3*n].y)/9}}this.nodes=e,this.colors=s}paintMesh(t,e){let s=(this.nodes.length-1)/3,r=(this.nodes[0].length-1)/3;if("bilinear"===this.type||s<2||r<2){let n;for(let o=0;o<s;++o)for(let s=0;s<r;++s){let r=[];for(let t=3*o,e=3*o+4;t<e;++t)r.push(this.nodes[t].slice(3*s,3*s+4));let i=[];i.push(this.colors[o].slice(s,s+2)),i.push(this.colors[o+1].slice(s,s+2)),(n=new m(r,i)).paint(t,e)}}else{let n,o,a,h,l,d,u;const x=s,g=r;s++,r++;let w=new Array(s);for(let t=0;t<s;++t){w[t]=new Array(r);for(let e=0;e<r;++e)w[t][e]=[],w[t][e][0]=this.nodes[3*t][3*e],w[t][e][1]=this.colors[t][e]}for(let t=0;t<s;++t)for(let e=0;e<r;++e)0!==t&&t!==x&&(n=i(w[t-1][e][0],w[t][e][0]),o=i(w[t+1][e][0],w[t][e][0]),w[t][e][2]=c(w[t-1][e][1],w[t][e][1],w[t+1][e][1],n,o)),0!==e&&e!==g&&(n=i(w[t][e-1][0],w[t][e][0]),o=i(w[t][e+1][0],w[t][e][0]),w[t][e][3]=c(w[t][e-1][1],w[t][e][1],w[t][e+1][1],n,o));for(let t=0;t<r;++t){w[0][t][2]=[],w[x][t][2]=[];for(let e=0;e<4;++e)n=i(w[1][t][0],w[0][t][0]),o=i(w[x][t][0],w[x-1][t][0]),w[0][t][2][e]=n>0?2*(w[1][t][1][e]-w[0][t][1][e])/n-w[1][t][2][e]:0,w[x][t][2][e]=o>0?2*(w[x][t][1][e]-w[x-1][t][1][e])/o-w[x-1][t][2][e]:0}for(let t=0;t<s;++t){w[t][0][3]=[],w[t][g][3]=[];for(let e=0;e<4;++e)n=i(w[t][1][0],w[t][0][0]),o=i(w[t][g][0],w[t][g-1][0]),w[t][0][3][e]=n>0?2*(w[t][1][1][e]-w[t][0][1][e])/n-w[t][1][3][e]:0,w[t][g][3][e]=o>0?2*(w[t][g][1][e]-w[t][g-1][1][e])/o-w[t][g-1][3][e]:0}for(let s=0;s<x;++s)for(let r=0;r<g;++r){let n=i(w[s][r][0],w[s+1][r][0]),o=i(w[s][r+1][0],w[s+1][r+1][0]),c=i(w[s][r][0],w[s][r+1][0]),x=i(w[s+1][r][0],w[s+1][r+1][0]),g=[[],[],[],[]];for(let t=0;t<4;++t){(d=[])[0]=w[s][r][1][t],d[1]=w[s+1][r][1][t],d[2]=w[s][r+1][1][t],d[3]=w[s+1][r+1][1][t],d[4]=w[s][r][2][t]*n,d[5]=w[s+1][r][2][t]*n,d[6]=w[s][r+1][2][t]*o,d[7]=w[s+1][r+1][2][t]*o,d[8]=w[s][r][3][t]*c,d[9]=w[s+1][r][3][t]*x,d[10]=w[s][r+1][3][t]*c,d[11]=w[s+1][r+1][3][t]*x,d[12]=0,d[13]=0,d[14]=0,d[15]=0,u=f(d);for(let e=0;e<9;++e){g[t][e]=[];for(let s=0;s<9;++s)g[t][e][s]=p(u,e/8,s/8),g[t][e][s]>255?g[t][e][s]=255:g[t][e][s]<0&&(g[t][e][s]=0)}}h=[];for(let t=3*s,e=3*s+4;t<e;++t)h.push(this.nodes[t].slice(3*r,3*r+4));l=y(h);for(let s=0;s<8;++s)for(let r=0;r<8;++r)(a=new m(l[s][r],[[[g[0][s][r],g[1][s][r],g[2][s][r],g[3][s][r]],[g[0][s][r+1],g[1][s][r+1],g[2][s][r+1],g[3][s][r+1]]],[[g[0][s+1][r],g[1][s+1][r],g[2][s+1][r],g[3][s+1][r]],[g[0][s+1][r+1],g[1][s+1][r+1],g[2][s+1][r+1],g[3][s+1][r+1]]]])).paint(t,e)}}}transform(t){if(t instanceof x)for(let e=0,s=this.nodes.length;e<s;++e)for(let s=0,r=this.nodes[0].length;s<r;++s)this.nodes[e][s]=this.nodes[e][s].add(t);else if(t instanceof g)for(let e=0,s=this.nodes.length;e<s;++e)for(let s=0,r=this.nodes[0].length;s<r;++s)this.nodes[e][s]=this.
nodes[e][s].transform(t)}scale(t){for(let e=0,s=this.nodes.length;e<s;++e)for(let s=0,r=this.nodes[0].length;s<r;++s)this.nodes[e][s]=this.nodes[e][s].scale(t)}}document.querySelectorAll("rect,circle,ellipse,path,text").forEach((r,n)=>{let o=r.getAttribute("id");o||(o="patchjs_shape"+n,r.setAttribute("id",o));const i=r.style.fill.match(/^url(s*"?\s*#([^s"]+)"?\s*)/),a=r.style.stroke.match(/^url(s*"?\s*#([^s"]+)"?\s*)/);if(i&&i[1]){const a=document.getElementById(i[1]);if(a&&"meshgradient"===a.nodeName){const i=r.getBBox();let l=document.createElementNS(s,"canvas");d(l,{width:i.width,height:i.height});const c=l.getContext("2d");let u=c.createImageData(i.width,i.height);const f=new b(a);"objectBoundingBox"===a.getAttribute("gradientUnits")&&f.scale(new x(i.width,i.height));const p=a.getAttribute("gradientTransform");null!=p&&f.transform(h(p)),"userSpaceOnUse"===a.getAttribute("gradientUnits")&&f.transform(new x(-i.x,-i.y)),f.paintMesh(u.data,l.width),c.putImageData(u,0,0);const y=document.createElementNS(t,"image");d(y,{width:i.width,height:i.height,x:i.x,y:i.y});let g=l.toDataURL();y.setAttributeNS(e,"xlink:href",g),r.parentNode.insertBefore(y,r),r.style.fill="none";const w=document.createElementNS(t,"use");w.setAttributeNS(e,"xlink:href","#"+o);const m="patchjs_clip"+n,M=document.createElementNS(t,"clipPath");M.setAttribute("id",m),M.appendChild(w),r.parentElement.insertBefore(M,r),y.setAttribute("clip-path","url(#"+m+")"),u=null,l=null,g=null}}if(a&&a[1]){const o=document.getElementById(a[1]);if(o&&"meshgradient"===o.nodeName){const i=parseFloat(r.style.strokeWidth.slice(0,-2))*(parseFloat(r.style.strokeMiterlimit)||parseFloat(r.getAttribute("stroke-miterlimit"))||1),a=r.getBBox(),l=Math.trunc(a.width+i),c=Math.trunc(a.height+i),u=Math.trunc(a.x-i/2),f=Math.trunc(a.y-i/2);let p=document.createElementNS(s,"canvas");d(p,{width:l,height:c});const y=p.getContext("2d");let g=y.createImageData(l,c);const w=new b(o);"objectBoundingBox"===o.getAttribute("gradientUnits")&&w.scale(new x(l,c));const m=o.getAttribute("gradientTransform");null!=m&&w.transform(h(m)),"userSpaceOnUse"===o.getAttribute("gradientUnits")&&w.transform(new x(-u,-f)),w.paintMesh(g.data,p.width),y.putImageData(g,0,0);const M=document.createElementNS(t,"image");d(M,{width:l,height:c,x:0,y:0});let S=p.toDataURL();M.setAttributeNS(e,"xlink:href",S);const k="pattern_clip"+n,A=document.createElementNS(t,"pattern");d(A,{id:k,patternUnits:"userSpaceOnUse",width:l,height:c,x:u,y:f}),A.appendChild(M),o.parentNode.appendChild(A),r.style.stroke="url(#"+k+")",g=null,p=null,S=null}}})}();        </script>      </svg>    </div>    <script>      let ws = new WebSocket('ws://esp32.local:81/');      ws.onopen = () => {        console.log('WebSocket opened');        const tspan2 = document.getElementById('tspan2');        if(tspan2) { tspan2.textContent = "Ready"; }      }      ws.onmessage = evt => console.log('From ESP32: ' + evt.data);        const rect = document.getElementById('rect36');      const marker = document.getElementById('rect41');      const hueText = document.getElementById('tspan41');        if(hueText) { hueText.textContent = "0Â°"; }      if(marker) { marker.setAttribute('transform', 'translate(-5,0)'); }      if(rect){        rect.addEventListener('click', function(evt) {          const svg = rect.ownerSVGElement;          const pt = svg.createSVGPoint();          pt.x = evt.clientX;          pt.y = evt.clientY;          const cursorpt = pt.matrixTransform(svg.getScreenCTM().inverse());          const minX = 6;          const maxX = 131;          const minT = -5;          const maxT = 120;          let cx = Math.max(minX, Math.min(maxX, cursorpt.x));          let translateX = minT + ((cx - minX) / (maxX - minX)) * (maxT - minT);          marker.setAttribute('transform', 'translate(' + translateX + ',0)');          const hue = Math.round(((cx - minX) / (maxX - minX)) * 360);          hueText.textContent = hue + 'Â°';          ws.send('hue,' + hue);        });      }        const stopEl = document.getElementById('g57');      stopEl && stopEl.addEventListener('click', function(evt) {          console.log('stop clicked');          ws.send('stop,');      });        const startEl = document.getElementById('g58');      startEl && startEl.addEventListener('click', function(evt) {          ws.send('start,');      });        const topY = 30;      const bottomY = 72;      const leftCircle = document.getElementById('g59');      const tspan37 = document.getElementById('tspan37');      leftCircle && leftCircle.addEventListener('click', function(evt) {          const svg = rect.ownerSVGElement;          const pt = svg.createSVGPoint();          pt.x = evt.clientX;          pt.y = evt.clientY;          const cursorpt = pt.matrixTransform(svg.getScreenCTM().inverse());          let v = 100 - ((cursorpt.y - topY) / (bottomY - topY)) * 200;          v = Math.max(-100, Math.min(100, v));          v = Math.round(v);          tspan37.textContent = v;          ws.send('fb,'+v);      });        const leftX = 81;      const rightX = 123;      const rightCircle = document.getElementById('g60');      const tspan39 = document.getElementById('tspan39');      rightCircle && rightCircle.addEventListener('click', function(evt) {          const svg = rect.ownerSVGElement;          const pt = svg.createSVGPoint();          pt.x = evt.clientX;          pt.y = evt.clientY;          const cursorpt = pt.matrixTransform(svg.getScreenCTM().inverse());          console.log(cursorpt.x);          let v = 100 - ((cursorpt.x - leftX) / (rightX - leftX)) * 200;          v = Math.max(-100, Math.min(100, v));          v = Math.round(v)*(-1);          tspan39.textContent = v;          ws.send('lr,'+v);      });        // WASD and arrow keys      document.addEventListener('keydown', function(event) {          switch (event.key) {            case 'ArrowUp':            case 'w':              tspan37.textContent = 100;              ws.send('fb,100');              break;            case 'ArrowDown':            case 's':              tspan37.textContent = -100;              ws.send('fb,-100');              break;            case 'ArrowLeft':            case 'a':              tspan39.textContent = -100;              ws.send('lr,-100');              break;            case 'ArrowRight':            case 'd':              tspan39.textContent = 100;              ws.send('lr,100');              break;            default:              break;          }      });        // For desktop, always apply the SVG styling      const svg = document.getElementById('svg1');      svg.removeAttribute('width');      svg.removeAttribute('height');      svg.style.width = '100vw';      svg.style.height = '100vh';      svg.style.maxWidth = '100vw';      svg.style.maxHeight = '100vh';      svg.style.display = 'block';    </script>      <style>      body, html {        margin: 0;        padding: 0;        width: 100vw;        height: 100vh;        overflow: hidden;      }      .svg-container {        width: 100vw;        height: 100vh;        display: flex;        align-items: center;        justify-content: center;      }      svg {        max-width: 100vw;        max-height: 100vh;        width: 136.90706mm;        height: 82.806686mm;        display: block;      }    </style>  </body></html>  )rawliteral");}
void setup(){  Serial.begin(9600);    // Set ESP32 to dual mode (AP+STA)  WiFi.mode(WIFI_AP_STA);    // Start the Access Point  WiFi.softAP("LucasPotato", "mypotato");  Serial.print("AP IP Address: ");  Serial.println(WiFi.softAPIP());    // Attempt to connect to STA network  WiFi.begin("mypotato", "coolpotato");  Serial.print("Connecting to STA network");  unsigned long startTime = millis();  while (WiFi.status() != WL_CONNECTED && (millis() - startTime) < 10000) {    delay(500);    Serial.print(".");  }  if(WiFi.status() == WL_CONNECTED) {    Serial.println("\nConnected to STA network");    Serial.print("STA IP Address: ");    Serial.println(WiFi.localIP());  } else {    Serial.println("\nSTA connection failed, continuing with AP only");  }    // Register mDNS with hostname "esp32" for both interfaces  if (MDNS.begin("esp32")) {    Serial.println("mDNS responder started: http://esp32.local/");  }  else {    Serial.println("Error setting up mDNS responder");  }    server.on("/", handleRoot);  server.begin();
  webSocket.begin();  webSocket.onEvent(webSocketEvent);
  pinMode(12, OUTPUT);  pinMode(14, OUTPUT);  pinMode(27, OUTPUT);  pinMode(13, OUTPUT);  Serial.println("Done starting up");}
void loop(){  server.handleClient();  webSocket.loop();}